## Slide 1: CPE 301
Lab #3 – The Memory Lab

## Slide 2: Contents:
Logic Levels
Breadboards
IC’s & Datasheets Reminders
How to wire switches
Hex -> Binary
The Lab

## Slide 3: Logic Levels
Digital logic -> 2 states
  On
  Off
Tri-State logic -> 3 states
  On
  Off
  Floating, High Impedance
 | Binary | Logic | Rails | TTL | CMOS | RS-232
ON | 1 | “High” | “Power” | +5V (2.0V-Vcc) | +3.3V (2/3Vdd-Vdd) | -15V to -3V
OFF | 0 | “Low” | “Ground” | 0V (0V-0.8V) | 0V (0-1/3Vdd) | +15V to +3V

## Slide 4: Breadboards
Rows & Rails:
Try to use jumpers as follows:
Power | Ground | Signal
Red, Orange, Yellow | Black, Brown, Blue, Green | White, Green, Purple, Blue, Yellow

## Slide 5: IC’s & Datasheets
Pin-out vs. Logic Diagram

## Slide 6: How to wire switches
Pull-up Resistors
What is the voltage at the pin when the switch is closed? Open?

## Slide 7: Hex -> Binary
Pay attention to MSB/LSB
Try to put MSB on LEFT
0x FF
0b 1111 1111
0d 256

## Slide 8: The Lab
RTFM
2 Circuits:
  16x8
  32x4
16x8 is simpler
Wire the switches first -> TEST & UNDERSTAND
  Write down -> OPEN = HIGH / LOW, CLOSED = HIGH / LOW
Then Wire the chips:
  Power & Ground
  Control Signals
  Data
Present the table of addresses and data in binary and hex to your TA

## Slide 9: Tables
# | HEX | BINARY
Address | Data | A3 | A2 | A1 | A0 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
# | HEX | BINARY
Address | Data | A4 | A3 | A2 | A1 | A0 | B3 | B2 | B1 | B0
1 |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |