## Slide 1: CPE 301
Lab #6 – The 7-Segment Lab
EEPROM
Buffers + Inverting + Common Anode + Safety
Port Selection
Switches vs Buttons
Debouncing

## Slide 2: Contents:
Overview
Notes on Code
7-Segment Displays
Switches
The Report
Tips

## Slide 3: Overview
Part 1 – Inputs from switches
  Enable port as input
  Enable pullup resistors on the input port
  TEST TEST TEST TEST
Part 2 – Output to LEDs
  Enable port as output
  TEST TEST TEST TEST

## Slide 4: Notes on Code
Use global variables!
  This isn’t 135
  Not a multi-user system
  Port definitions
  Rename variables to make sense
Add comments!
  Broken + No Comments = 0.0
  Broken + Useful Comments = 0.5

## Slide 5: 7 Segment Displays
Datasheet on webcanvas
Common Anode
  common pin connects to +5V
  LED turns on when pin is grounded
74LS240 Buffer & Inverter
  Circuit protection & inverted logic for common anode

## Slide 6: Switches
Use the Arduino’s internal pullups

## Slide 7: Include in your report
Map of port bits to LED segments (i.e. PK0 = Segment “A”)
Code pasted into your report as normal text
Screenshot of the terminal window at the bottom of the IDE showing that it compiled

## Slide 8: Tips
Assemble and test in order:
  Get the switches working
    Use a scope to verify the pin is high when the switch is open, low when the switch is closed
    Use Serial.println() to make sure you can read the pin register and get the result you expect
  Hookup the 74LS240, resistors, and LED
    Test the inputs of the 74LS240 without the Arduino (just 5V and ground)
  Setup the Arduino, and test port outputs with a scope
  Lastly, connect the Arduino and the 74LS240
Numbers can be represented in binary!
0d10 = 0x0A = 0b 0000 1010