## Slide 1: CPE 301
Timer Interrupts

## Slide 2: ToDo -
Merge UART and Timer Lab
Timer Lab - instead of taking inputs from the Serial library, use your UART functions
Instead of using while loop for timing highs and lows, use interrupts
Interrupts use the TOV flags in TIMSK and TIFR
Interrupt - ISR(TIMER_OVF_vect);
Inside function -
  Stop Timer,
  Load Counter
  Toggle output to high/low when
  Start Timer

## Slide 3: Interrupt Function
Define it as -
ISR(TIMER_OVF_vect){ …………………. …………………. }
NO return types, ensure NAME is exactly as shown.
Gets called as soon as the TIMER_OVF_vect is set, automatically

## Slide 4: Interrupt Function
Difference between ISR and my_delay
my_delay function needs to be explicitly called in the main loop
my_delay function needed a while loop for waiting until the OVERFLOW bit was set
ISR gets called as soon as OVERFLOW bit is set, so no need to be called anywhere explicitly and no while loop.