## Slide 1: CPE 301
LAB #1

## Slide 2: LAB #1
Lab reports will be due on the Thursday following the lab
Lab report format
No more than 3 to a group, 2 is preferred
Individual work
  Build your own circuits
  Take your own pictures
  Write your own reports

## Slide 3: Lab Safety Quiz

## Slide 4: Lab Equipment
Power Supply
Function Generator
Oscilloscope
Probes/Leads

## Slide 5: Power Supply
3 fixed outputs, 1 Variable Input
Use the right leads

## Slide 6: Function Generator
Generates waveforms
  Sine, square, triangle
Two outputs
  TTL
  50 Ohm
Used for…
  Diagnostics
  Clock Sources
  References
Use the right leads

## Slide 7: Oscilloscope
Generates a two dimensional plot of a signal, usually voltage over time
What is a signal?
  Digital/Analog
Uses:
  Shape/Amplitude/Frequency
  Timing between two events
  Observing noise

## Slide 8: Oscilloscope
Acquiring a waveform:
  Signal conditioning
  A/D Conversion
  Storing the samples in memory
  Displaying the samples

## Slide 9: Oscilloscope Characteristics
Bandwidth
  Frequency range
  Bandwidth > 5x the highest frequency that needs to be measured
Rise time
  Edge speed
  Scope rise time < (signal rise time / 5)
Sample rate
  Nyquist –> sample rate = 2x highest signal frequency (minimum)
  Tektronix–> sample rate = 5x highest signal frequency (marketing?)
  Analog Engineers –> sample rate = 10x highest frequency (rule-of-thumb)
Record length
  Number of samples stored for one waveform

## Slide 10: Oscilloscope Display

## Slide 11: Oscilloscope Demo