ADC LAB

---
What is an ADC?
- Analog to digital converter.
- Takes an analog values between 0-5V and convert it to a 10 bit unsigned int (0-1023).
- Two serial ports 0-15 for reading analog input.
- WE can read the value from an analog inputs using all 16 pins or both analog ports.
- We will be using ADCSRA, ADCSRB and ADMUX registers.

---
ADCSRA
- Analog to digital register A.
- Used for enabling and disabling ADC mode using ADEN.
- Start Conversion using ADSC.
- Use ADFR to select the free running mode or single conversion mode(use single conversion mode).
- We will not be using interrupt in this lab.
- Use the minimum pre-scaler.

---
ADCSRB
- We will be using bit 3:0
- Bit 3 (MUX5) is used for selecting the channel and gain bits.
- Bits 2:0 to set free running mode.

---
ADMUX
- Bit 7:6 are used for voltage reference ( use internal reference)
- Reset the ADLAR for right adjustment.
- Bit 2:0 is used for selecting the input channel(pin).
- To select channel between 0-7 use MUX5 (ADCSRB) should be 0 and bit 2:0 should be assigned the value between 0-7.
- To select channel 8-15 set the MUX5 (ADCSRB) and bit 2:0 should be assigned the value between 0-7.

---
ADC Read
- Takes the channel as a argument
- Assign the appropriate value to MUX5 and Admux bits 2:0.
- Start the conversion by setting ADSC (ACDSRA).
- Wait for the conversion to finish.
- Return the value in ADC_DATA register.

---
Results
- Use your own putchar function to transmit the data back to your computer to display the ADC values.
- You have to extract each value one by one (like previous lab) to transmit the data. e.g. 1011 should be transferred as ‘1’, ‘0’, ‘1’ and ‘1’.
- Use the serial plotter to analyze the adc conversion.
- You can use a flash light on the photo resistor to see the impact of voltage variation due to ambience.

---
Photo-resistor
- Light controlled variable resistor.
- Resistance decreases with increase in light intensity.
- Make a voltage divider using a coaxial resistor and connect it with your arduino.
- Circuit diagram in lab manual.

---
What we are expecting
- Full understanding of the ADC registers.
- Functional code and circuit.
- Should function with different input channels.

---
Tips
- Start with the the serial library to test your conversions.
- Test your UART code separately before integrating with the conversion code.
- Test with the single channel first.