## Slide 1: CPE 301
Lab #5 - Timers & Tones

## Slide 2: Contents
Lab Overview
Applications
Timers
Hints

## Slide 3: Lab Overview
Write a program to:
Receive a character over the serial port
Generate a tone on PB6 which corresponds to the input character
Additional requirements:
  At boot, PB6 should be low until a key is pressed
  After the user enters ‘q’, PB6 should go low and stay low until another key is pressed
Test with an oscilloscope, then with a speaker
  Don’t forget a series resistor when connecting the speaker
  The speaker is only 8 ohms and can damage the 2560!

## Slide 4: Additional Requirements
At boot, PB6 should be low until a key is pressed
After the user enters ‘q’, PB6 should go low and stay low until another key is pressed
Test with an oscilloscope, then with a speaker
  Don’t forget a series resistor when connecting the speaker
  The speaker is only 8 ohms and can damage the 2560!

## Slide 5: Applications
Embedded Systems!
  Real-time performance
  No Operating System
  Events occur when they’re supposed to
  Generic Applications
    Counting Events
    Timing between events
    Generating Frequencies
  Robotics
    Hardware Synchronization (Cameras / IMU / GPS)
  Communication
    High Speed Protocols

## Slide 6: Timers
Dedicated peripheral inside the 2560
6 Registers to control and interface with the timer
Have a lot of advanced functionality we won’t use
  Output compare
  External Triggering
  Interrupts (Lab #9)

## Slide 7: Timer Registers
TCNT = Timer Count Register
  16 bit register
  With a prescaler of 1, increments with every clock tick
  When TCNT == 64K, TOV goes high
TCCR1A-C = Timer/Counter Control Registers
  Contains bits which control the trimer
  Start/stop
  Prescaler
  Etc
TIFR = Timer Interrupt Flag Register
  Contains the TOV bit
TIMSK = Timer Interrupt Mask Register
  Don’t forget to disable the TOV interrupt!

## Slide 8: Timers
Prescalers – Given a prescaler, what is the maximum amount of delay possible?
  FCLK = 16MHz (62.5nSec)
  Max TCNT = 65535
Bigger prescaler = less precision, but shorter max delay
Goal: Find the smallest prescaler that can produce every frequency

## Slide 9: Reading from Serial

## Slide 10: Timer Delay Steps
Stop the Timer
Load the counts
Start the timer (with a prescaler)
Wait for TOV
Stop the Timer
Reset TOV

## Slide 11
Hints
Hook up the speaker to the function generator & scope to get a better idea of what you're trying to do
Calculate the delay for each frequency
Calculate the smallest prescaler that works for all frequencies
Given the prescaler, calculate the # ticks required for each frequency
Go back to blinky, get a simple square wave using port manipulation and a simple delay function
Modify the delay function to delay precisely
Decode the value returned by Serial.read()

## Slide 12
Important Pages
These pages in the Atmel datasheet will prove helpful
16-Bit Timer Description – Page 133
Normal Mode Description – 17.1.9, Page 145
Register Description – 17.11, Page 154
Clock Select – 17.11.8, Page 157
Prescalers – 18, Page 164